Matlab Simulation of Cameras Tracking Volume
Program to calculate the approximate tracking volume obtained by a tracking system camera setup. Current values are valid for Flex13 Optitrack tracking system (8 cameras).

C1 to C8 are all the cameras present in the drone arena. “deltaY” is the horizontal pointing angle of the camera located in the corners. Distance from C1-C3 that we call in the software L1 is 4.25 m. While distance C3- C5, L2 = 5.40 m.
Any camera is defined with the following parameters:
- Field Of View - defined as horizontal and vertical field of views
- Camera Range - the maximum distance at the camera can track
- Pose - position of the center and orientation of the camera
Matrix for 8 M = matrix { center_x # center_y # center_z # att_Yaw # att_pitch # att_roll # fov Horiz # fov Vert ## 0.0+DE # L1-DE # 3.05 # -45.0 # 4.16+fov_v/2.0 # 0.0 # fov_h # fov_v ## 0.0+DE # L1/2.0 # 3.05 # 0.0 # 4.16+fov_v/2.0 # 0.0 # fov_h # fov_v ## 0.0+DE # 0.0+DE # 3.05 # 45.0 # 4.16+fov_v/2.0 # 0.0 # fov_h # fov_v ## L2/2.0 # 0.0+DE # 3.05 # 90.0 # 4.16+fov_v/2.0 # 0.0 # fov_h # fov_v ## L2-DE # 0.0+DE # 3.05 # 135.0 # 4.16+fov_v/2.0 # 0.0 # fov_h # fov_v ## L2-DE # L1/2.0 # 3.05 # 180.0 # 4.16+fov_v/2.0 # 0.0 # fov_h # fov_v ## L2-DE # L1-DE # 3.05 # 225.0 # 4.16+fov_v/2.0 # 0.0 # fov_h # fov_v ## (L2/2.0) # L1-DE # 3.05 # 270.0 # 4.16+fov_v/2.0 # 0.0 # fov_h # fov_v } cameras:

Tracking Volume is defined as the global origin and the size of the volume to be tracked:
Tracking Volume = matrix{origx # origy # origz # sizex # sizey # sizez}
The basic idea behind this software is to check in the whole volume for every voxel in the space spacefied in the tracking_volume variable. The plot shows the portion of the space (as voxels) that is seen by at least min_cameras_point = 3 cameras (the parameter can be change to any integer value).
Every voxel is a 3D point p_w = (xp,yp,zp). In the function camera_point_visible_bool( camera, p_w ) the point is transformed from world coordinates to camera coordinates. Then it is checked whether the points is inside the camera_range and the field of view of the camera.
The size of the Voxel is set as voxel_size=2^(Vox_Size-1)*[1 1 1] .